## Slide 1
REVERSE
ENGINEERING
Applied to STOIC
SWWG Community of Interest
Max Duverneuil

## Slide 2
WHAT IS REVERSE ENGINEERING?
Understanding the fundamentals
The process of analyzing a system to identify its components and their interrelationships, then creating representations of the system at a higher level of abstraction.
Static Analysis
Examine code, firmware, and data structures without execution
Dynamic Analysis
Observe system behavior at runtime — signals, I/O, memory
Protocol Analysis
Decode communication formats, command structures, and data flows

## Slide 3
WHY RE FOR SOTIC?
3-30
kHz
VLF Band Range
10k+
km
Propagation Distance
N
layers
System Complexity
Legacy System Understanding
Many VLF collection systems predate modern documentation standards
Vulnerability Assessment
Identify weaknesses in RF processing chains and firmware
Interoperability
Enable integration with new hardware and modern processing pipelines
Performance Optimization
Discover undocumented features and potential performance gains

## Slide 4
TYPICAL VLF COLLECTION SYSTEM ARCHITECTURE
Typical signal flow — each stage is an RE target
Antenna
& Front-End
ADC &
Digitizer
DSP /
FPGA
Signal
Processing
Data Store
& Export
KEY RE TARGETS PER STAGE
Front-End — Antenna tuning parameters, filter coefficients, impedance matching networks
ADC — Sample rates, bit depth, clock sources, calibration routines
DSP/FPGA — Firmware bitstreams, filter chains, demodulation algorithms
Signal Processing — Detection thresholds, classification logic, noise reduction
Data Store — File formats, metadata schemas, compression methods

## Slide 5
RE METHODOLOGIES
Structured approaches for systematic analysis
Binary Analysis
Disassembly of embedded firmware
Control flow graph reconstruction
String & symbol extraction
Cross-reference mapping
Signal Analysis
Spectral decomposition of VLF captures
Modulation scheme identification
Timing & synchronization recovery
Noise floor characterization
Protocol Decoding
Bus traffic capture (SPI, I2C, UART)
Command-response pattern mining
State machine reconstruction
Packet format identification
Black-Box Testing
Input fuzzing & boundary testing
I/O stimulus-response mapping
Performance profiling under load
Error injection & recovery analysis

## Slide 6
TOOLS OF THE TRADE
Category
Tools
Focus
Disassemblers / Decompilers
Ghidra, IDA Pro, Binary Ninja, radare2
Essential for firmware RE
Protocol Analyzers
Wireshark, Saleae Logic, sigrok, GNU Radio
Bus & signal capture
SDR Platforms
USRP, HackRF, RTL-SDR, KiwiSDR
VLF signal capture & replay
Debuggers / Emulators
GDB, OpenOCD, QEMU, J-Link
Runtime inspection
Signal Processing
MATLAB, GNU Octave, SciPy, NumPy
DSP algorithm analysis
Hex / Binary Editors
HxD, 010 Editor, ImHex, binwalk
Firmware & data format analysis
Pro Tip: Ghidra's built-in processor modules support many embedded architectures found in VLF collection hardware. Custom loader scripts can handle proprietary firmware formats.

## Slide 7
RE ENTRY POINTS
Where to start when analyzing a system like STOIC
01
External Interfaces
Identify all physical and logical I/O: serial ports, Ethernet, USB, debug headers (JTAG/SWD), RF connectors
02
Firmware Extraction
Dump flash/EEPROM via debug interfaces, read firmware update packages, capture OTA updates
03
Communication Buses
Tap internal buses (SPI, I2C, UART) between modules. Map command/data flow between DSP, MCU, and host
04
Signal Chain Probing
Capture raw ADC output, intermediate DSP stages, and processed output. Compare against known VLF signals
05
Configuration Files
Extract and analyze config files, calibration data, frequency tables, and filter parameters

## Slide 8
SIGNAL PROCESSING PIPELINE RE
Raw
Samples
ADC Output
Band-Pass
Filter
VLF Isolation
Down-
Conversion
Baseband
Matched
Filter
Detection
Feature
Extraction
Classification
CRITICAL RE ANALYSIS AREAS
Filter Coefficients
Recover FIR/IIR tap values from firmware or FPGA bitstreams. Validate against expected VLF band characteristics.
Sample Rate & Resolution
Determine ADC clock rates, decimation factors, and effective bandwidth through timing analysis.
Detection Algorithms
Identify threshold logic, CFAR implementations, and signal classification decision trees.
Calibration Data
Locate and decode calibration tables, antenna gain patterns, and environmental correction factors.

## Slide 9
COMMON CHALLENGES
Pitfalls and obstacles specific to VLF RF system RE
Proprietary Architectures
Custom DSP cores and undocumented instruction sets in legacy VLF hardware
HIGH
FPGA Bitstream Opacity
Reconstructing logic from synthesized bitstreams is non-trivial; limited tooling for older FPGA families
HIGH
Analog/Digital Boundary
VLF front-end behavior is heavily influenced by analog characteristics that don't appear in digital analysis
MED
Undocumented Data Formats
Proprietary IQ sample formats, custom compression, and non-standard metadata encoding
MED
Anti-Tamper Mechanisms
Readout protection, encrypted firmware, fused debug ports, and watchdog-triggered wipes
HIGH

## Slide 10
LEGAL & ETHICAL CONSIDERATIONS
LEGAL FRAMEWORK
DMCA § 1201 exemptions for security research
CFAA boundaries — authorized vs. unauthorized access
Export control regulations (ITAR / EAR) for RF systems
Contractual obligations and NDA scope
Patent landscape awareness
ETHICAL GUIDELINES
Responsible disclosure of discovered vulnerabilities
Minimize impact on operational systems
Document and share findings with authorized stakeholders
Respect classification levels and need-to-know
Maintain chain of custody for extracted data

## Slide 11
BEST PRACTICES & TAKEAWAYS
Start with the Known
Use published VLF standards (e.g., MSK, FSK modulation) as reference points. Compare observed signals against expected characteristics. Reference: United States Frequency Allocations
Layer Your Analysis
Combine static firmware analysis with dynamic signal capture. Cross-validate findings at every stage.
Automate & Script
Build reusable Ghidra scripts, GNU Radio flow graphs, and automated test harnesses. Reproducibility is critical.
Document Everything
Maintain detailed RE journals. Record hypotheses, test results, memory maps, and signal captures with timestamps.
Collaborate Across Disciplines
VLF RE spans RF engineering, embedded systems, and software. Bring the full team to bear on complex systems.